868MHz  Antenna

| Ⅰ●Electrical Specifications |
| --- |
| Model | ESG-868-05 |
| Frequency Range | 865-868MHz |
| Gain | 3dBi |
| V.S.W.R | ≤2.0 |
| Radiation | OMNI |
| Polarization | Vertical |
| Maximum Input Power | 50W |
| Impedance | 50Ώ |
| Operating Temperature | -40℃ to+70℃ |
| Connector | SMA Male |
| Cable Length | 3m |
| Mount way | Stick |
| Π●Mechanical Specifications |
| Antenna Dimension | 22×115mm |
| Weight | 45g |
| Rated Wind Velocity | / |

二、PRODUCT SPECIFICATION CHART

1.Picture

2.Dimension

三、PATTERN

1.V.S.W.R

2.Direction